Guide to continuing the laser scan calibration

by Daniel Mäki

supervised by:
Felix Meßmer
Calibration explained

In order for an advanced robotic system to manipulate or interact with its environment, information about its environment must first be obtained. Acquiring this information is done via the sensors of the robot. The sensors on a robot obtain data which is processed, producing a certain output. Depending on the robots current goal, the output data is send to the manipulators of the robot. A manipulator is an object, for example a robot arm, that manipulates or interacts with the robots environment. In order for the robot to send the correct output to a manipulator, the robot has to know where the manipulator is located. In other words, if the robot wants to grab a glass from a table, it first needs to know where its arm and camera are located in order to detect and grasp the glass correctly. Therefore, when building a robot, one has to provide a position for every component. However, when specifying a position, one has to understand that a position is actually made out of two points. Meaning, a position is actually the distance between two points. Now, the best way to build a robust robot is to create a common reference point. Meaning that each component of the robot has a position with respect to the common reference point. This, for example, also allows the robot to give coordinates to objects in its environment because everything can be calculated back to this reference point. This is where calibration comes into play.
After one has manually measured all distances between every component and reference point, these measurements can then be improved with calibration. For a robot like the Care-O-Bot, it is important to achieve very accurate manipulation and therefore, it is highly effective to calibrate the components by using an algorithm that automatically finds and adjusts the accuracy of each manual measurement.

Background

At Fraunhofer IPA, we use the open source calibration algorithm code from Willow Garage from Vijay Pradeep. At Fraunhofer, a student (Sebastian Haug) writing his Bachelor thesis, had implemented Vijays algorithm (also used on the PR2) to the Care-O-Bot 3-6. Sebastian was able to successfully calibrate the robot arm, torso and camera.
After Sebastian left Fraunhofer, a student (Jannik Abbenseth) took his place and continued Sebastians work by further improving the calibration algorithm. Janniks modifications allowed the calibration procedure to be run on multiple different robotic platforms like the rob@work and other Care-O-Bot versions.
When Jannik finished, another student (Daniel Mäki) continued the calibration topic. Daniel mainly focused on the calibration of the laser scanners. This report gives a detailed explanation on the procedure of the laser scanner calibration.

Calibration algorithm

For a detailed explanation on the calibration algorithm, read the conference paper from Vijay Pradeep.

Calibrating a multi-arm multi-sensor robot: A Bundle Adjustment Approach
Conference Paper by Vijay Pradeep
http://www.willowgarage.com/sites/default/files/calibration.pdf

The calibration object

As explained in Vijays paper, a fixed point in the robots environment is required to use the calibration algorithm. This fixed point can be obtained by detecting a predefined object in the robots environment.
In our case, the object exists of three standing cylinders with on top a checkerboard. The three cylinders all have a different radius, the small cylinder has a radius of 3cm, the medium cylinder has a radius of 6cm and the large cylinder has a radius of 9cm (0.03m, 0.06m and 0.09m). The three cylinders are setup as an equilateral triangle, meaning that all sides have the same length and all three angles are exactly 60 degrees (30/pi). The lengths of the sides are measured from each center of the cylinders (40cm). The checkerboard has a grid of 6x9 black and white squares. The cylinders are used by the laser scanner and the checkerboard is used by the camera.

A 3d-model of the calibration object can be found in:
/cob_calibration/cob_laser_calibration/objects/cal_obj.urdf

To spawn the calibration object in Gazebo (Gazebo must be running) write in terminal:
roslaunch cob_laser_calibration cal_obj.launch

The calibration object can be modified as desired but it must fulfill the following conditions:
- The calibration object must exist of three cylinders (small, medium and large) and one checkerboard.
- The checkerboard has to be placed on top of the cylinders so that it is visible to the camera.
- The cylinders have to be setup straight, so that they are standing.
- The size of the cylinder radii must grow linearly, meaning, medium=2*small and large=3*small.
- The centers of the cylinders must be positioned in an equilateral triangle.
- When viewing the calibration object from above, the large cylinder must be at the bottom aligned with the x-axis, the small cylinder on the left side and the medium cylinder on the right side.
- The center of the triangle and the center of the checkerboard are aligned in the z-axis with the checkerboard orientated so that one of its short sides points towards the large cylinder.

Note that all changes, like height, radii and distance, which are made to the calibration object must also be applied to the determine_cal_obj_pose.py script.

The laser scanner

In order to understand the next chapter where we go through the detection of the calibration object, one should first know how the laser scanner works.
The laser scanner of the Care-O-Bot returns a horizontal line of points. Each point has an angle and a distance. Using these two values, we can compute the x and y coordinates of each point and create a 2D projection. When the laser scanner makes its measurements between 5 and 10 hertz, it increments its angle each time with 0.5 degrees (0.00872666668147 RAD), starting from -135 degrees (-2.35619997978 RAD) until +135 degrees (2.35619997978 RAD).

Detecting the calibration object

Before explaining the scripts used for detecting the calibration object, we shall first explain the approach that we took on determining the pose of the calibration object. Because the laser scan only provides a horizontal line of depth points, BLABLABLA

The following description is a walk-through for the scripts used to determine the calibration object pose. We shall start with the upper level script. The script returns the quaternion coordinates of the calibration object with respect to the base (/base_footprint).

The file path of this script is:
/cob_calibration/cob_laser_calibration/scripts/

To run the script in terminal, write:
rosrun cob_laser_calibration determine_cal_obj_pose.py

Package name = "cob_laser_calibration"
Node name = "laser_scan_calibration"

Imports:
- LaserScan message, is found in sensor_msgs/msg
- Uses all classes from visualize_laser_scan.py, located in the same directory as determine_cal_obj_pose.py

Global variables:
- The scanner_location will determine whether you detect the calibration object with the front or rear laser scanner.
- The resolution is probably something you will have to change if you want to switch between visualization or precise detection. A resolution of 200 or lower will give you an image for visualizing the actual laser scan image. For making precise detections, I would suggest you use a resolution between 1000 and 2000. A resolution of 1000 will return calculations with an accuracy of 1mm.
- If the calibration objects properties are changed, all changes must also be applied in this script under cylinder.

The script contains comment lines with numbering which correspond to the following numbers:

1. The script starts by retrieving the pose of the laser scanner with respect to “/base_footprint”.
2. Then we create a callback function for retrieving the sensor data from the laser scanner. For this we use the LaserScan message.
3. Next we create a loop for detecting the calibration object and appending each successful detection to a list until either the success_counter or the fail_counter has exceeded its limit.
4. Within this loop, we first get an average scan, removing most of the noise that comes with each individual scan. This uses the class Get_laserscan from visualize_laser_scan.py.
5. In each new round, we create a new image containing the laser scan data. This uses the class Visualize_laserscan from visualize_laser_scan.py.
6. After creating the image, we use the Detect_calibration_object class from visualize_laser_scan.py for detecting the pose of the calibration object within the image.
7. When the pose is received, we convert the calibration object pose into Euler coordinates, append this to the successful_detections list and increment the success_counter. However, if the calibration object was not detected successfully, we will not append this pose to the list and we increment the fail_counter.
8. Regardless of which counter limit is exceeded, we calculate the average pose from all poses in the successful_detections list and also calculate the standard devision for each detection.
9. Once that is done, we draw the average calibration object pose in the image.
10. Then convert the Euler pose into a quaternion pose
11. Then finally, print the results

Now we shall proceed with explaining the three classes from visualize_laser_scan.py used in step 4, 5 and 6.

The file path of this script is:
/cob_calibration/cob_laser_calibration/scripts/

Imports:
LaserScan message, is found in sensor_msgs/msg

The class Get_laserscan:

  1. When initializing this class, all data used in this class is set back to zero so that a new average scan can be calculated.
  2. Each time the append_laserscan function is run, the new laser scan is averaged out over the amount of current scans creating a new average of all current laser scans plus the new scan.

The class Visualize_laserscan:

  1. This class takes many of the global variables. All variables are being setup in the __init__ function and also here, all data used for new calculations are being reset.
  2. The main function of this class (convert_to_image) executes four other functions where we calculate the x and y coordinates of the image points, create the image, interpolate all points and draw the fixed objects into the image.
  3. In calculate_image_points, by using the average laser scan measurements, we can compute the x and y coordinates for all laser scan points which will define most of our image that we will create later on.
    1. By starting with the minimum laser scan angle, we increment the angle until we reach the maximum angle of the laser scanner and create a list from all angles.
    1. For each angle we also have the distance from the laser scanner to the measured point. Using both distance and angle, we can compute x with: distance*cos(angle) and y with: distance*sin(angle).
  4. In create_image, we create the image and set the position of the laser scanner in the image. All points will be with respect to this point called origin.
  5. In interpolate_points, we draw a line between each two points.
    1. For every two points we compute the distance and angle between the two points using both x and y values. The distance is calculated by getting the hypotenuse and the angle is calculated by using arctangent.
    2. To draw a line between the two points, we create a while loop that colors every pixel between the two points. A pixel has a value of one, so each round we add cos(angle) to the x-axis and sin(angle) to the y-axis creating a line along the hypotenuse.
  6. In draw_fixed_object, we draw the laser scanner, center of the base and a box around the base representing the range of the robots body.
  7. In draw_calibration_object, we first calculate the x,y and yaw coordinates of the calibration object before drawing the circles and triangle.
  8. In show_image, we show a visualization of the image containing the laser scan, laser scanner, base and calibration object. However, this image is only shown if the resolution is 200 or smaller.

The class Detect_calibration_object:

  1. Setup all variables and clear old data.
  2. In detect_cal_object, we execute the function for detecting the calibration objects cylinders and convert the cylinder data into a calibration object pose.
    1. When all cylinders are received, we can calculate the center of the calibration object by adding up all cylinder coordinates and dividing them by three.
    2. After the x and y coordinates of the calibration object center are determined, we still need to determine the rotation of the calibration object. In our case we only need yaw and this is calculated by getting the arctangent of the calibration object center and cylinder and adding the fixed angle of the position of the cylinder within the calibration object.
  1. In detect_cal_obj_cylinders, BLABLABLA

Further improvements

BLABLABLA

Next steps

Create script for calculating all points on the checkerboard from the returned value of the determine_cal_obj_pose.py

A physical model of the calibration object has to be created. It is extremely important that all calibration object dimensions correspond with the variables in the determine_cal_obj_pose.py

BLABLABLA